Accuracy and Precision in the Determination of the Density of Water

PA State Standards Addressed:

3.4.10.A	Explain concepts about the structure and properties of matter.

3.4.12.A		Apply concepts about the structure and properties of matter.

Quantify the properties of matter by applying mathematical formulas.

3.7.10.B	Apply appropriate instruments and apparatus to examine a variety of objects and processes.

Explain the need to estimate measurements within error of various instruments.

Introduction:

Mass and volume are extrinsic properties which depend on the quantity of a substance.  Density, which is the ratio of mass to volume (D=m/V), is an intrinsic property.  The density of a substance is a constant and is characteristic of the substance.  Therefore, density can be used to aid in the identification of a substance.  However, the density of a substance may vary with its temperature.  In this lab the mass and volume of water will be measured, and the density of the water will be calculated.  This value will be compared to the accepted density of water at the relevant temperature.  The accuracy and precision of the measurements will also be determined.  Accuracy refers to the closeness of a measurement to the true or accepted value, while the precision refers to the repeatablility of a measurement.  Multiple trials of each method will be done to determine the precision.

In this experiment, two instruments will be used to measure the mass: a top loading balance, and an analytical balance.  Four different instruments will be used to measure volume: a beaker, a graduated cylinder, a glass pipet, and an automatic pipet.

Guiding Questions:

- Which combination of instruments will be the least accurate?  Why?

- Which combination of instruments will be the most accurate?  Why?

- Which combination of instruments will be the least precise?  Why?

- Which combination of instruments will be the most precise?  Why?

Equipment/Materials:

30 mL beaker				deionized water

250 mL beaker			10 mL automatic pipet

10 mL graduated cylinder		top loader balance

volumetric pipet			analytical balance

thermometer				plastic dropper

Safety:

- Goggles should be worn in the lab when using glassware.

Procedure and Data:

- Place 150 – 200 mL of deionized water in a 250 mL beaker.

- Measure and record the temperature of the water.

Water Temperature:  _______ ˚C

Beaker and Top Loading Balance

- Place a clean, dry 30 mL beaker on the top loading balance. Tare.

- Remove the beaker from the balance, and pour 10 mL of deionized water into it, using a dropper if necessary. Record the volume in the data table to the correct number of significant digits.

- Place the beaker on the balance and record the mass of the water in the data table.  Do not round!

- Discard the water in the sink and repeat for trials 2 & 3.  It is not necessary to dry the inside of the beaker when using a top loading balance.

Trial		   Vol	(mL)		Mass	(g)	Density (g/mL)

| 1 |  |  |  |
| --- | --- | --- | --- |
| 2 |  |  |  |
| 3 |  |  |  |

Average Density  _______g/mL

Graduated Cylinder and Top Loading Balance

- Look at the writing on the 10 mLgraduated cylinder.

  - If it says TC, it is designed To Contain the volume of liquid that is read. If the cylinder says TC, tare it on the balance.

  - If it says TD, it is designed To Deliver the volume of liquid that is read.  If the cylinder says TD, tare the 30mL beaker on the balance.

- Pour 10mL of deionized water in the graduated cylinder, using a dropper if necessary.  Record the volume on the data table to the correct number of significant digits.

- To determine the mass:

  - If the cylinder says TC, put the cylinder on the balance and record the mass in the data table.  Do not round!

  - If the cylinder says TD, pour the water into the tared beaker, and place the beaker on the balance. Record the mass in the data table.  Do not round!

- Repeat for trials 2 & 3.

Trial		   Vol	(mL)		Mass	(g)	Density (g/mL)

| 1 |  |  |  |
| --- | --- | --- | --- |
| 2 |  |  |  |
| 3 |  |  |  |

Average Density  _______g/mL

Pipet and Top Loading Balance

- Place a clean, dry 30 mL beaker on the top loading balance.  Tare.

- Using a volumetric pipet, add 10 mL of deionized water to the 30 mL beaker.  Record the volume of water in the data table to the correct number of significant digits.

- Place the beaker on the balance, and record the mass in the data table.  Do not round!

- Repeat for trials 2 & 3.

Trial		   Vol	(mL)		Mass	(g)	Density (g/mL)

| 1 |  |  |  |
| --- | --- | --- | --- |
| 2 |  |  |  |
| 3 |  |  |  |

Average Density  _______g/mL

Automatic Pipet and Top Loading Balance

- Place a clean, dry 30 mL beaker on the top loading balance.  Tare.

- Using the automatic pipet, add 10 mL of deionized water to the 30 mL beaker.  Record the volume of water in the data table to the correct number of significant digits.

- Place the beaker on the balance, and record the mass of the water in the data table.  Do not round!

- Repeat for trials 2 & 3.

Trial		   Vol	(mL)		Mass	(g)	Density (g/mL)

| 1 |  |  |  |
| --- | --- | --- | --- |
| 2 |  |  |  |
| 3 |  |  |  |

Average Density  _______g/mL

Repeat each of the above sets of procedures using the analytical balance in place of the top loading balance.

Beaker and Analytical Balance

Trial		   Vol	(mL)		Mass	(g)	Density (g/mL)

| 1 |  |  |  |
| --- | --- | --- | --- |
| 2 |  |  |  |
| 3 |  |  |  |

Average Density  _______g/mL

Graduated Cylinder and Analytical Balance

Trial		   Vol	(mL)		Mass	(g)	Density (g/mL)

| 1 |  |  |  |
| --- | --- | --- | --- |
| 2 |  |  |  |
| 3 |  |  |  |

Average Density  _______g/mL

Pipet and Analytical Balance

Trial		   Vol	(mL)		Mass	(g)	Density (g/mL)

| 1 |  |  |  |
| --- | --- | --- | --- |
| 2 |  |  |  |
| 3 |  |  |  |

Average Density  _______g/mL

Automatic Pipet and Analytical Balance

Trial		   Vol	(mL)		Mass	(g)	Density (g/mL)

| 1 |  |  |  |
| --- | --- | --- | --- |
| 2 |  |  |  |
| 3 |  |  |  |

Average Density  _______g/mL

Calculations:

1.	Actual density of water at recorded temperature from Appendix 1 : ________ g/mL

2.	Calculate the % error (accuracy) for each density average value.

% ERROR = Actual - Ave calc density / actual density x 100%

Top loading		     Analytical

| Beaker |  |  |
| --- | --- | --- |
| Graduated Cylinder |  |  |
| Pipet |  |  |
| Automatic Pipet |  |  |

3.	Calculate the precision (standard deviation) of each set of data

standard deviation =[((x - x1)²)/(n - 1)]

where x = density for each individual trial

x1= average density

n = number of trials

Top loading		     Analytical

| Beaker |  |  |
| --- | --- | --- |
| Graduated Cylinder |  |  |
| Pipet |  |  |
| Automatic Pipet |  |  |

Questions:

- Which combination of instruments was the least accurate?  How do you know?

- Which combination of instruments was the most accurate? How do you know?

- Which combination of instruments was the least precise?  How do you know?

- Which combination of instruments was the most precise?  How do you know?

- Did the mass of water shown on the analytical balance tend to decrease with time?  If so, why?  If not, why not?

References:

Snelling, C. (2008, June 14). Density of Water (g/mL) vs. Temperature (°C). Retrieved June 1, 2011, from http://www2.volstate.edu/CHEM/Density_of_Water.htm

Appendix 1

# Density of Water (g/mL) vs. Temperature (°C)

(from Handbook of Chemistry and Physics, 53rd Edition, p. F4)
Whole degrees are listed down the left hand side of the table, while tenths of a degree are listed across the top.
So to find the density of water at say 5.4 °C, you would first find the whole degree by searching down the left hand 
column until you reach '5'.  Then you would slide across that row until you reach the column labeled '0.4'.  
The density of water at 5.4 °C is 0.999957 g/mL.

|  | 0.0 | 0.1 | 0.2 | 0.3 | 0.4 | 0.5 | 0.6 | 0.7 | 0.8 | 0.9 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 0 | 0.999841 | 0.999847 | 0.999854 | 0.999860 | 0.999866 | 0.999872 | 0.999878 | 0.999884 | 0.999889 | 0.999895 |
| 1 | 0.999900 | 0.999905 | 0.999909 | 0.999914 | 0.999918 | 0.999923 | 0.999927 | 0.999930 | 0.999934 | 0.999938 |
| 2 | 0.999941 | 0.999944 | 0.999947 | 0.999950 | 0.999953 | 0.999955 | 0.999958 | 0.999960 | 0.999962 | 0.999964 |
| 3 | 0.999965 | 0.999967 | 0.999968 | 0.999969 | 0.999970 | 0.999971 | 0.999972 | 0.999972 | 0.999973 | 0.999973 |
| 4 | 0.999973 | 0.999973 | 0.999973 | 0.999972 | 0.999972 | 0.999972 | 0.999970 | 0.999969 | 0.999968 | 0.999966 |
| 5 | 0.999965 | 0.999963 | 0.999961 | 0.999959 | 0.999957 | 0.999955 | 0.999952 | 0.999950 | 0.999947 | 0.999944 |
| 6 | 0.999941 | 0.999938 | 0.999935 | 0.999931 | 0.999927 | 0.999924 | 0.999920 | 0.999916 | 0.999911 | 0.999907 |
| 7 | 0.999902 | 0.999898 | 0.999893 | 0.999888 | 0.999883 | 0.999877 | 0.999872 | 0.999866 | 0.999861 | 0.999855 |
| 8 | 0.999849 | 0.999843 | 0.999837 | 0.999830 | 0.999824 | 0.999817 | 0.999810 | 0.999803 | 0.999796 | 0.999789 |
| 9 | 0.999781 | 0.999774 | 0.999766 | 0.999758 | 0.999751 | 0.999742 | 0.999734 | 0.999726 | 0.999717 | 0.999709 |
| 10 | 0.999700 | 0.999691 | 0.999682 | 0.999673 | 0.999664 | 0.999654 | 0.999645 | 0.999635 | 0.999625 | 0.999615 |
| 11 | 0.999605 | 0.999595 | 0.999585 | 0.999574 | 0.999564 | 0.999553 | 0.999542 | 0.999531 | 0.999520 | 0.999509 |
| 12 | 0.999498 | 0.999486 | 0.999475 | 0.999463 | 0.999451 | 0.999439 | 0.999427 | 0.999415 | 0.999402 | 0.999390 |
| 13 | 0.999377 | 0.999364 | 0.999352 | 0.999339 | 0.999326 | 0.999312 | 0.999299 | 0.999285 | 0.999272 | 0.999258 |
| 14 | 0.999244 | 0.999230 | 0.999216 | 0.999202 | 0.999188 | 0.999173 | 0.999159 | 0.999144 | 0.999129 | 0.999114 |
| 15 | 0.999099 | 0.999084 | 0.999069 | 0.999054 | 0.999038 | 0.999023 | 0.999007 | 0.998991 | 0.998975 | 0.998959 |
| 16 | 0.998943 | 0.998926 | 0.998910 | 0.998893 | 0.998877 | 0.998860 | 0.998843 | 0.998826 | 0.998809 | 0.998792 |
| 17 | 0.998774 | 0.998757 | 0.998739 | 0.998722 | 0.998704 | 0.998686 | 0.998668 | 0.998650 | 0.998632 | 0.998613 |
| 18 | 0.998595 | 0.998576 | 0.998558 | 0.998539 | 0.998520 | 0.998501 | 0.998482 | 0.998463 | 0.998444 | 0.998424 |
| 19 | 0.998405 | 0.998385 | 0.998365 | 0.998345 | 0.998325 | 0.998305 | 0.998285 | 0.998265 | 0.998244 | 0.998224 |
| 20 | 0.998203 | 0.998183 | 0.998162 | 0.998141 | 0.998120 | 0.998099 | 0.998078 | 0.998056 | 0.998035 | 0.998013 |
| 21 | 0.997992 | 0.997970 | 0.997948 | 0.997926 | 0.997904 | 0.997882 | 0.997860 | 0.997837 | 0.997815 | 0.997792 |
| 22 | 0.997770 | 0.997747 | 0.997724 | 0.997701 | 0.997678 | 0.997655 | 0.997632 | 0.997608 | 0.997585 | 0.997561 |
| 23 | 0.997538 | 0.997514 | 0.997490 | 0.997466 | 0.997442 | 0.997418 | 0.997394 | 0.997369 | 0.997345 | 0.997320 |
| 24 | 0.997296 | 0.997271 | 0.997246 | 0.997221 | 0.997196 | 0.997171 | 0.997146 | 0.997120 | 0.997095 | 0.997069 |
| 25 | 0.997044 | 0.997018 | 0.996992 | 0.996967 | 0.996941 | 0.996914 | 0.996888 | 0.996862 | 0.996836 | 0.996809 |
| 26 | 0.996783 | 0.996756 | 0.996729 | 0.996703 | 0.996676 | 0.996649 | 0.996621 | 0.996594 | 0.996567 | 0.996540 |
| 27 | 0.996512 | 0.996485 | 0.996457 | 0.996429 | 0.996401 | 0.996373 | 0.996345 | 0.996317 | 0.996289 | 0.996261 |
| 28 | 0.996232 | 0.996204 | 0.996175 | 0.996147 | 0.996118 | 0.996089 | 0.996060 | 0.996031 | 0.996002 | 0.995973 |